## Slide 1: EDGE COMPUTING & EDGE CACHING: Οφέλη, Προκλήσεις και λύσεις.
Ηλίας-Ελιας Μπαρμπάρ
1115201200118

## Slide 2: General Idea:
5G requirements being covered through Edge computing & Edge caching.
Workload on the edges of the mobile network. Computing and Caching.
Many benefits for Server Providers, Users and Enterprises but not without difficulties and negative aspects.

## Slide 3: 5G vs 4G, and the new requirements for 5G:
5G has extreme requirements: -massive broadband-critical machine communication-massive communication
The new standard has identified three primary requirements: massive machine-to-machine (M2M) communications for Internet of Things (IoT) applications, ultra-low latency enabling life-saving car-to-car connectivity, for example, and gigabit speeds (high-bandwidth mobile broadband).
Before 5G we hosted third party authorized apps in the operators’ network, now the new meeting point is where operators’ apps and context providers collaborate.
It no longer makes sense for all the data collected from those devices to be processed in a national or regional data center. Edge computing exists to bring the data center closer to where it’s needed, thus allowing for faster processing time.
THE CURRENT TOPOLOGY OF ENTERPRISE NETWORKS There are three places most enterprises tend to deploy and manage their applications and services:
On-premises, where data centers house multiple racks of servers, where they're equipped with the resources needed to power and cool them, and where there's dedicated connectivity to outside resources
Colocation facilities, where customer equipment is hosted in a fully managed building where power, cooling, and connectivity are provided as services
Cloud service providers, where customer infrastructure may be virtualized to some extent, and services and applications are provided on a per-use basis, enabling operations to be accounted for as operational expenses rather than capital expenditures
The architects of edge computing would seek to add their design as a fourth category to this list: one that leverages the portability of micro data centers (µDC) and small form-factor servers to reduce the distances between the processing point and the consumption point of functionality in the network. If their plans pan out, they seek to accomplish the following:

## Slide 4: ΩΦΕΛΗ ΤΟΥ EDGE COMPUTING & CACHING:
Οφέλη των Server Providers – Οφέλη των Επιχειρήσεων – Οφέλη των Χρηστών
Edge computing allows for faster monetization of 5G investments by delivering next-gen applications to consumers and, more importantly, enterprise customers.
No matter the location, the goal remains the same — to provide computing power as close to the device producing data as possible to increase speed and lower latency.
POTENTIAL BENEFITS
Minimal latency. The problem with cloud computing services today is that they're slow, especially for artificial intelligence-enabled workloads. This essentially disqualifies the cloud for serious use in deterministic applications, such as real-time securities markets forecasting, autonomous vehicle piloting, and transportation traffic routing. Processors stationed in small data centers closer to where their processes will be used could open up new markets for computing services that cloud providers haven't been able to address up to now.
Simplified maintenance. For an enterprise that doesn't have much trouble dispatching a fleet of trucks or maintenance vehicles to field locations, micro data centers (µDC) are designed for maximum accessibility, modularity, and a reasonable degree of portability. They're compact enclosures, some small enough to fit in the back of a pickup truck, that can support just enough servers for hosting time-critical functions, that can be deployed closer to their users. Conceivably, for a building that presently houses, powers, and cools its data center assets in its basement, replacing that entire operation with three or four µDCs somewhere in the parking lot could be an improvement.
Cheaper cooling. For large data center complexes, the monthly cost of electricity used in cooling can easily exceed the cost of electricity used in processing. The ratio between the two is called power usage effectiveness (PUE). At times, this has been the baseline measure of data center efficiency (although in recent years, surveys have shown fewer IT operators know what this ratio means). Theoretically, it may cost a business less to cool and condition several smaller data center spaces than it does one big one. Plus, due to the peculiar ways in which some electricity service areas handle billing, the cost per kilowatt may go down across the board for the same server racks hosted in several small facilities rather than one big one. A recent white paper published by Schneider Electric [PDF] assessed all the major and minor costs associated with building traditional and micro data centers. While an enterprise could incur just under $7 million in capital expenses for building a traditional 1 MW facility, it would spend just over $4 million to facilitate 200 5 KW facilities.
That’s a great question. You can boil it down to four key reasons. The first reason is speed. I touched on this before, but edge computing reduces latency because data doesn’t have to travel over a network to a remote data center or the cloud for processing. The second reason is security. We could see improved security at the edge because the data stays closer to where it was created. The third is related to scalability. Edge computing is fundamentally ‘distributed computing,’ meaning it improves the resiliency, reduces network load, and is easier to scale. And finally, it matters because it lowers cost. Data transmission costs are lower because the amount of data transferred back to a central location for storage is reduced.
ACCELERATE TIME TO REVENUE Scalable next-generation technology platforms that enable rapid service delivery.
CREATE NEW REVENUE STREAMS Leverage our industry expertise to build new managed services for end customers.
DIGITAL TRANSFORMATION Technology solutions that create a more agile service provider and deliver business outcomes.

## Slide 5: Προκλήσεις του Edge Computing & Caching:
5G has extreme requirements: -massive broadband-critical machine communication -massive communication
Network operators and developers are in a bit of a staring contest as it relates to the delivery of 5G. Application developers are waiting for the platform so they can begin developing apps around it. Most service providers, meanwhile, are waiting on specific use cases to justify initial buildouts. Both sides are waiting for advances from the other.
Huge Cost for Server Providers
Set of technology that is deployed at the edge of a server providers infrastructure. Big investment that needs to be monetized. The end user will have increased cost. Enterprise customers are the main customers then the end user. They need to figure out how to monetize it (server providers). Challenges are mainly cost and scalability.
Billions of new connected devices are creating and collecting data that needs to be processed. Imagine if all that processing takes place in the cloud. The network would very quickly get overwhelmed, regardless of how powerful it is. We will run into issues with network congestion and latency. With edge computing, we push some processing closer to the devices to help eliminate the latency and congestion problems, and improve performance of the applications running on those devices. This is a bit of an oversimplification, but you can see the benefit. Another advantage has to do with the availability of services on devices. Because slow response time and outages are unacceptable, if you move the computation as close to the device or even on the device, we can improve availability.
It’s easy to think edge computing magically solves many problems that cloud computing can’t, but there’s a trade-off due to the highly distributed nature of edge systems. Each of the edge nodes are not completely independent, as each may need to share information with other nodes, and keeping data consistent is a challenge. The question is: How do I coordinate a large number of edge computing systems while still allowing them to work independently? This is a problem that has perplexed designers of distributed systems for many years. People call this the distribution, consistency, and synchronization problem.
The number of edge computing systems will be high, so any solution will need to scale greatly. Altogether, this is a big problem to solve.
Remote availability of three-phase power. Servers capable of providing cloud-like remote services to commercial customers, regardless of where they're located, need high-power processors and in-memory data, to enable multi-tenancy. Probably without exception, they'll require access to high-voltage, three-phase electricity. That's extremely difficult, if not impossible, to attain in relatively remote, rural locations. (Ordinary 120V AC current is single-phase.) Telco base stations have never required this level of power up to now, and if they're never intended to be leveraged for multi-tenant commercial use, then they may never need three-phase power anyway. The only reason to retrofit the power system will be if edge computing is viable. But for widely distributed Internet-of-Things applications such as Mississippi's trials of remote heart monitors, a lack of sufficient power infrastructure could end up once again dividing the "have's" from the "have-not's."

## Slide 6: ΛΥΣΕΙΣ:
We deploy application in close proximity in order to provide real-time services to satisfy the demanding requirements for ultra-low latency and high bandwidth also automation and scalability and offers additional privacy and security and ensures significant cost saving.
In fact, given its role in the 5G delivery ecosystem — if mobile operators are racing to be first to deliver a true 5G network, edge computing may very well be the vehicle they use to get to the finish line — edge solutions need to be vertically focused and strategically deployed.
Ideally, perhaps after a decade or so of evolution, edge computing would bring fast services to customers as close as their nearest wireless base stations. We'd need massive fiber optic pipes to supply the necessary backhaul, but the revenue from edge computing services could conceivably fund their construction, enabling it to pay for itself.

## Slide 7: IN CONCLUSION:
Tying it all together:
Similar to 5G, edge computing is not a single technology, but a set of technologies being deployed in unison to achieve a business outcome. And to achieve the scale needed with edge deployments, white box hardware will undoubtedly play a part.
The disaggregated nature of 5G adds further complexity. White box hardware alongside open source software stacks provide significantly more innovation and development opportunities. But as simple as it may sound, it is complicated.
Disaggregating software from hardware allows service providers to realize cost savings by deploying original design manufacturer (ODM) equipment while leveraging the power of software to become a nimbler operator that can provide best-of-breed solutions tailored to industry verticals.
Service providers desire the value white box can deliver, but typically can’t commit to the labor-intensive processes needed to validate and deploy white box solutions effectively nor able to dedicate the time or resources needed for ongoing support.
Deploying white box-based solutions is building something new and unknown. For service providers, it’s critical they have confidence the solutions they deploy will work as intended once deployed in the field. Operators need an experienced integrator that can oversee multi-vendor solutions, validate and ensure design requirements are met, rollout the solution quickly at scale, optimize the solution on an ongoing basis and provide technical support between various vendors.

## Slide 11: RefERENCES:

## Slide 12
Edge computing & edge cashing στο δίκτυο. (Μαζί με την συνεχή εγκατάσταση του 5G δικτύου, έρχεται και το edge computing and cashing για να πραγματοποιησει το όραμα του νεου σχεδιασμό computing του δικτυου. Η ιδέα είναι να αρχίσει να μεταφέρεται η επεξεργασία δεδομενων στα άκρα του δικτύου και όταν χρειαζεται να υπαρχει καποιο caching συστημα που να ελαχιστοποιει επανηλημένη προσβαση σε βαθια σημεια του δικτυου.)
Εργασία στα άκρα του δικτύου και caching.
Πολλά θετικά για Server Providers, Χρήστες και Επιχειρήσεις όχι όμως χωρις δυσκολίες και αρνητικά στοιχεία ( Αυτό το καινουργιο συστημα ερχεται με πολλα θετικα και θα αλλαξει τελειως τον τροπο πουσκεφτομαστε και πρατουμαι στο δικτυο όχι όμως χωρις τις δυσκολιες και τα αρνητικα του.)